Three-Year Wet Sulfate Deposition

1989 to 1991 vs 2014 to 2016

Source: NADP/NTN & PRISM, 2018

Acid Deposition

As SO₂ and NOₓ gases react in the atmosphere with water, oxygen, and other chemicals, they form acidic compounds that are deposited to the earth's surface in the form of wet and dry acid deposition.

Long-term monitoring network data show significant improvements in the primary indicators of acid deposition. For example, wet sulfate deposition (sulfate that falls to the earth through rain, snow, and other precipitation) has decreased in much of the Ohio River Valley and Northeastern United States due to SO₂ emission reductions achieved through implementation of the Acid Rain Program (ARP), the Clean Air Interstate Rule (CAIR) and the Cross-State Air Pollution Rule (CSAPR). Some of the most dramatic reductions have occurred in the mid-Appalachian region, including Maryland, New York, West Virginia, Virginia, and most of Pennsylvania. Along with wet sulfate deposition, precipitation acidity, expressed as hydrogen ion (H+ or pH) concentration, has also decreased by similar percentages.

Monitoring Networks

The Clean Air Status and Trends Network (CASTNET) provides long-term monitoring of regional air quality to determine trends in atmospheric concentrations and deposition of nitrogen, sulfur, and ozone in order to evaluate the effectiveness of national and regional air pollution control programs. CASTNET now operates more than 90 regional sites throughout the contiguous United States, Alaska, and Canada. Sites are located in areas where urban influences are minimal.

The National Atmospheric Deposition Program/National Trends Network (NADP/NTN) is a nationwide, long-term network tracking the chemistry of precipitation. The NADP/NTN provides concentration and wet deposition data on hydrogen ion (acidity as pH), sulfate, nitrate, ammonium, chloride, and base cations. The NADP/NTN has grown to more than 250 sites spanning the United States, Canada, Puerto Rico, and the Virgin Islands.

Together, these complementary networks provide long-term data needed to estimate spatial patterns and temporal trends in total deposition.